## Slide 1: Acadia DOE OBD Data Exploratory Analysis
Dingchao Zhang 11/12/2016

## Slide 2: Acadia DOE Data Scope
7 System Errors, all Event Driven
8 Parameters
124 Tests from 3/25/2015 to 10/2/2015

## Slide 3: Plots Types
Individual System Error Plots:
Mean, Max, Min range Plot( Mean,Max,Min on the same plot)
All System Errors Plot:
Ppk Trend Plot
Mean+-1Std Plot
Mean, Max, Min range Plot( Mean,Max,Min on the same plot)
R output graphs can be found in \\CIDCSDFS01\EBU_Data01$\NACTGx\Common\DL_Diag\Data Analysis\Storage\Knowledge base\Acadia DOE\graphs

## Slide 4: Ppk Trend All System Error Plot
Observations:
NOX_OUT_SENSOR_IR_LO_MOTOR_ERR has a few tests whose Ppk are below 1.5
NOX_IN_SENSOR_DITHER_ERR has one test whose Ppk is below 1.5
All other System Errors have Ppk above 1.5 in all tests

## Slide 5: MinMaxMean Range All System Error Plot
Observations:
NOX_IN_SENSOR_DITHER_ERR has larger variance than other System Errors
NOX_IN_SENSOR_DITHER_ERR appears to have a mean below 1000 or above 1500 in the first few tests, while in the more recent tests, the mean appears between 1000 and 1500

## Slide 6: Mean+-1Std All System Error Plot
Observations:
NOX_IN_SENSOR_DITHER_ERR has the largest variance, and the variance appears gets larger as tests carry on

## Slide 7: NOX_IN_SENSOR_DITHER_ERR
Observations:
NOX_IN_SENSOR_DITHER_ERR appears to have a mean below 1000 or above 1500 in the first few tests, while in the more recent tests, the mean appears between 1000 and 1500
NOX_IN_SENSOR_DITHER_ERR’s variance appears gets larger as tests carry on

## Slide 8: SCR_EFFICIENCY4_DEGRADED_ERR
Observations:
SCR_EFFICIENCY4_DEGRADED_ERR appears not making many decisions in the first few tests
Majority of tests show the maximum values are about 2 times larger than mean values, with a few tests showing maximum values as large as 3 times of mean values.

## Slide 9: SCR_CAT_SUBSTRATE_MISSING_ERR
Observations:
SCR_CAT_SUBSTRATE_MISSING_ERR appears not making many decisions in the first few tests
SCR_CAT_SUBSTRATE_MISSING_ERR has a few tests records showing minimum or maximum value at a larger difference than mean values

## Slide 10: NOX_IN_SENSOR_IR_LO_MOTOR_ERR
Observations:
NOX_IN_SENSOR_IR_HI_MOTOR_ERR’s performances are correlated with NOX_IN_SENSOR_IR_LO_MOTOR_ERR’s performances

## Slide 11: NOX_IN_SENSOR_IR_HI_MOTOR_ERR
Observations:
NOX_IN_SENSOR_IR_HI_MOTOR_ERR’s performances are correlated with NOX_IN_SENSOR_IR_LO_MOTOR_ERR’s performances
A few tests showing very large maximum values

## Slide 12: NOX_OUT_SENSOR_IR_LO_MOTOR_ERR
Observations:
NOX_OUT_SENSOR_IR_LO_MOTOR_ERR’s performances are highly correlated with NOX_OUT_SENSOR_IR_HI_MOTOR_ERR’s performances
A few tests showing very large maximum values

## Slide 13: NOX_OUT_SENSOR_IR_HI_MOTOR_ERR
Observations:
NOX_OUT_SENSOR_IR_LO_MOTOR_ERR’s performances are highly correlated with NOX_OUT_SENSOR_IR_HI_MOTOR_ERR’s performances
A few tests showing very large maximum values

## Slide 14: Unsupervised Machine Learning Practices
To provide insight into the 1st goal of the Acadia DOE tests listed by Paul
Tools:
Python scikit, pandas, numpy, matplot packages are used to complete the following analysis.
Scripts are not attached.

## Slide 15: Hierarchical Clustering
Bottom-Up (agglomerative): Starting with each item in its own cluster, find the best pair to merge into a new cluster. Repeat until all clusters are fused together. We begin with a distance matrix which contains the distances between every pair of objects in our database.
Dendrogram of Acadia DOE Tests using OBD Data

## Slide 16: Hierarchical Clustering Groups
Refers to the color in the dendrogram in slide 15

## Slide 17: Principle Component Analysis
Principal component analysis (PCA) is a statistical procedure that uses an orthogonal transformation to convert a set of observations of possibly correlated variables into a set of values of linearly uncorrelated variables called principal components.
The major goal of principal components analysis is to reveal hidden structure in a data set. In so doing, we may be able to
• identify how different variables work together to create the dynamics of the system
• reduce the dimensionality of the data
• decrease redundancy in the data
• filter some of the noise in the data
The principal components are orthogonal because they are the eigenvectors of the covariance matrix.

## Slide 18: PCA Factors Loading Analysis and Scatter Plot of 1st, 2nd Components of PCA
Factors Loading Score Plot
PCA Scatter Plot
X axis : 1st component of Eigenvector
Y axis: 2nd component of Eigenvector

## Slide 19: K Means Clustering

## Slide 20: K Means Clustering, K = 2

## Slide 21: K Means Clustering Subgroups, K = 2

## Slide 22: K Means Clustering Subgroups, K = 3

## Slide 23: K Means Clustering, K = 3

## Slide 24: K Means Clustering Subgroups, K = 3

## Slide 25: K Means Clustering, K = 4

## Slide 26: K Means Clustering Subgroups, K = 4

## Slide 27: K Means Clustering, K = 5

## Slide 28: K Means Clustering Subgroups, K = 5